## Slide 1: Detailed Analysis and Comparison of Chiplet Interconnect Standards: UCIe, BoW, and OpenHBI
Sravya Koduru BU ID: U85097768 Dhiraj Simhadri BU ID: U38209521

## Slide 2: Introduction
Importance of chiplet-based architectures Need for efficient interconnect standards Purpose of the report

## Slide 3: UCIe Overview
Introduction: - Launched in March 2022 - Consortium members: Intel, AMD, ARM, etc. Key Features: - Standardized protocol layers - Supports 16 GT/s and 32 GT/s per lane - Compatible with PCIe and CXL protocols

## Slide 4: BoW Overview
Introduction: - Developed under the Open Compute Project (OCP) Key Features: - Emphasizes simplicity with minimal protocol overhead - Utilizes parallel interfaces - Supports up to 16 Gbps per wire

## Slide 5: OpenHBI Overview
Introduction: - Standardized by JEDEC - Version: OpenHBI-2 as of October 2023 Key Features: - High bandwidth per pin (up to 8 Gbps) - Optimized for memory and processor integration - Utilizes wide interfaces (e.g., 1024 pins)

## Slide 6: Bandwidth Comparison Table
Standard | Data Rate per Lane/Wire/Pin | Number of Lanes/Wires/Pins | Aggregate Bandwidth
UCIe | 32 GT/s per lane | Up to 32 lanes | >1 Tbps
BoW | 16 Gbps per wire | 256 wires | ~4 Tbps
OpenHBI | 8 Gbps per pin | 1024 pins | ~8 Tbps

## Slide 7: Latency and Power Efficiency
Latency: - UCIe: ~10-20 ns total - BoW: ~2-5 ns total - OpenHBI: ~2 ns physical layer Power Efficiency: - UCIe: ~0.5 pJ/bit - BoW: 0.5 - 1 pJ/bit - OpenHBI: ~1 pJ/bit

## Slide 8: Scalability and Interoperability
UCIe: - High scalability (lanes and protocols) - Strong interoperability (multi-vendor support) BoW: - Moderate scalability (physical constraints) - Limited interoperability OpenHBI: - High scalability (with complex design) - Moderate interoperability (memory-focused)

## Slide 9: AI Application Analysis
Requirements: - High bandwidth - Low latency - Power efficiency - Scalability Suitability: - UCIe: Excellent - BoW: Very Good - OpenHBI: Excellent

## Slide 10: HPC Application Analysis
Requirements: - Extreme bandwidth - Low latency - Scalability - Interoperability Suitability: - UCIe: Excellent - BoW: Good - OpenHBI: Very Good

## Slide 11: Comparative Summary
Criteria | UCIe | BoW | OpenHBI
Data Rate per Lane/Wire/Pin | 32 GT/s per lane | 16 Gbps per wire | 8 Gbps per pin
Aggregate Bandwidth | >1 Tbps | ~4 Tbps | ~8 Tbps
Latency | ~10-20 ns total | ~2-5 ns total | ~2 ns physical layer
Power Efficiency | ~0.5 pJ/bit | 0.5 - 1 pJ/bit | ~1 pJ/bit
Scalability | High | Moderate | High (with complexity)
Interoperability | Strong | Limited | Moderate
Suitability for AI | Excellent | Very Good | Excellent

## Slide 12: Sprint 3 and beyond
Simulation and Design of Interconnect Fabric:
Design a prototype interconnect fabric using one or more of these standards.
Simulate the performance of the chosen interconnects in 2.5D and 3D stacked environments using industry-standard EDA tools.
Implement the interconnect in a virtual chiplet-based system (using tools like Gem5 or MATLAB/Simulink).
Evaluate Performance Metrics:
Measure and analyze the bandwidth, latency, and power consumption of each interconnect standard.
Assess the feasibility of integrating chiplets from different vendors, considering modularity and compatibility.
Simulate the thermal impact of the interconnect in advanced packaging environments (using tools like ANSYS or COMSOL).